## Slide 1
Nitrogen Oxides in the Troposphere
sources, distributions, impacts, and trends
Lecture at the ERCA 2018
Grenoble, January 19, 2018
Andreas Richter
Institute of Environmental Physics
University of Bremen
Bremen, Germany
( richter@iup.physik.uni-bremen.de )

## Slide 2: Overview
What is NOx?
What is it doing in the troposphere?
Why should we care?
Where does it come from?
How can it be measured?
Is it changing with time?

## Slide 3: Simplified NOx Chemistry in the Troposphere
HO2 or RO2
NO3
N2O5
NO
NO2
O3
H2O, surface
night
NO
NO2
O3
hν
HNO3
NH3
OH
day
nitrate aerosol
HONO
OH
hν
surface reactions
adapted from M. Jenkin
emission
RO2NO2
RO2
e.g. PANs => transport
HOONO

## Slide 4: Some facts on NOx in the Troposphere
NO and NO2 are rapidly converted into each other and are therefore combined to
NOx = NO + NO2
the ratio [NO] / [NOx] is about 0.2 at the surface but increases towards higher altitudes (temperature dependence of O3 + NO reaction)
the atmospheric lifetime of NOx is short close to the surface (hours) and increases towards higher altitudes (days)
lifetime is longer in winter than in summer (lower [OH])
the short lifetime results in little transport, both vertically and horizontally, at least in the form of NOx => NOx is found close to its sources
PAN has a long lifetime and can be transported and re-release NOx when temperature increases
Ehhalt D.H. et al., (1992) Sources and distribution of Nox in the upper troposphere at northern mid-latitudes. J Geophys Res 97: 3725–3738

## Slide 5: Why should we care about NOx in the Troposphere?
NOx
is a key species in tropospheric ozone formation
leads to formation of HNO3 and thereby acid rain
contributes to eutrophication
acts directly as a greenhouse gas (NO2, at least locally)
acts indirectly on climate through
  ozone formation
  Impact on [OH] and thus lifetime of other greenhouse gases such as CH4
can contribute to aerosol formation

## Slide 6: The Role of NOx in Ozone Chemistry
Background conditions
photolysis of NO2 is the only known way to produce O3 in the troposphere
O3, NO2, and NO are in photostationary state (Leighton relationship):
    [O3][NO2] / [NO] = JNO2 / kO3 + NO
at very low [NO] / [O3] ratio, destruction of O3 by HO2 dominates over O3 production
Polluted conditions
if NO is oxidized to NO2 by HO2 or RO2 instead of O3, ozone is catalytically formed by NO
how much O3 can be formed in the presence of NOx is eventually limited by the amount of CO, CH4, and other hydrocarbons available
at high NOx concentrations, O3 levels are reduced by reaction with NO and NO2 in particular at night (“titration”)

## Slide 7: NOx and acid Rain
normal rain should have a pH of about 5, but much lower values are often observed in industrialised areas
SO2 emissions have been the main reason for acid rain
as SO2 emissions decreased, NOx became relatively more important
HNO3 is formed through several paths and its wet and dry deposition is one of the main sinks for nitrogen oxides:
  NO2 + OH + M → HONO2 + M
  N2O5(g) + H2O (g,l) → 2HNO3(g, aq)
  NO3(aq) + H2O(l) → HNO3(aq) + OH(aq)
  NO3 + RH → HNO3(g) + R
the effects of acid rain are most pronounced on freshwater fish and forest ecology, but also on buildings

## Slide 8: NOx and acid Rain: Example
Nitrate deposition in China 2010 – 2012 based on OMI NO2 observations and precipitation
Liu et al., Remote sensing of Environemnt, 199,93-106, 2017

## Slide 9: Sources of NOx in the Troposphere
Main sources of NOx (in Tg N / yr) are
fossil fuel combustion 22.0 (15 – 29)
fires 6.7 (3 – 10)
microbial soil emissions 5.5 (3.3 – 7.7)
lightning 2.0 (1 – 4)
oxidation of biogenic NH3 1.0 (0.5 – 1.5)
aircraft 0.5 (0.5 – 0.6)
stratosphere 0.5 (0.4 – 0.6)
R. Delmas et al., Nutrient Cycling in Agroecosystems, 48, 51 – 60, 1997

## Slide 10: Anthropogenic NOx Sources
anthropogenic emissions concentrated in a few industrialised areas
largest emissions in cities and from power plants
emissions per capita very unevenly distributed => future?
http://www.environment-agency.gov.uk/commondata/103196/1162897?referrer=/yourenv/eff/1190084/air/1158715/1162725/
UK, 2004
http://www.mnp.nl/edgar/model/v32ft2000edgar/edgarv32ft-prec/edgv32ft-nox-map.jsp
including biomass burning!
road transport has large importance
energy production is second, depending on energy mix

## Slide 11: Anthropogenic NOx Sources: Example
Normalised tropospheric NO2 columns retrieved from GOME satellite measurements show clear weekly cycle over industrialised areas
anthropogenic NOx emissions dominate
Beirle et al., Atmos. Chem. Phys., 3, 2225–2232, 2003

## Slide 12: Anthropogenic NOx sources: Lifetime
For large and isolated point sources, OMI observations can be sorted by wind direction
Plume model provides lifetime
Column + lifetime gives emissions
Beirle, et al., Megacity Emissions and Lifetimes of Nitrogen Oxides Probed from Space, Science 333, 1737 (2011); DOI:10.1126/science.1207824

## Slide 13: Soil Sources of NOx
NO and N2O are emitted from microbial activities in the soil, both during nitrification (NH4+ → NO3-) and denitrification (NO3- → N2)
function of soil moisture and texture, inorganic nitrogen availability, the carbon to nitrogen ratio, temperature and precipitation
typical parameterisation using T, precipitation and fertilisation
usually observed as strong pulses after fertilisation and rain
in ecosystems with dense vegetation cover (e.g. rain forests), part of the NOx emitted is lost by NO2 deposition
NOx soil emissions seem to be underestimated in current models
potential for increases as use of fertilizers increases, but strong dependence on actual practices used

## Slide 14: Soil Sources of NOx: Example
Chouteau, Hill and Liberty Counties in North-Central Montana, USA
harvested cropland, low population density, no large stationary NOx sources
NO2 columns retrieved from SCIAMACHY satellite data are large after fertilisation and subsequent precipitation
Bertram, T. H., et al., (2005), Satellite measurements of daily variations in soil NOx emissions, Geophys. Res. Lett., 32, L24812, doi:10.1029/2005GL024640

## Slide 15: NOx from Biomass Burning
biomass burning is happening on large scales on a regular basis as part of
  agricultural practices
  wild fires
  domestic fires
it is a significant source of NOx
the amount of NOx emitted per biomass burned varies strongly between different biomass types (savannah, tropical rain forests, boreal forests)
large amounts of NOx are emitted in the tropics, much less e.g. in Alaska or Siberia
in big fires, enough heat is produced to start pyroconvection and to inject NOx in the upper troposphere
fires can be observed by their IR signature (i.e. MODIS), NO2 can be observed by UV/vis observations

## Slide 16: NOx from Biomass Burning
Schreier, S.F., : The empirical relationship between satellite-derived tropospheric NO2 and fire radiative power and possible implications for fire emission rates of NOx, Atmos. Chem. Phys., 14, 2447-2466, doi:10.5194/acp-14-2447-2014, 2014

## Slide 17: NOx from Lightning
at very high temperatures (> 2000 K) O2 + M → O + O + M O + N2 → NO + N N + O2 → NO + O (Zel’dovitch mechanism).
lightning NOx is computed from the product of lightning dissipation energy and NO yield per Joule of discharge
estimates have varied dramatically in the past: 1.2 Tg ... 200 Tg N / yr
recent estimates cluster around 2..5 Tg N / yr
estimates are based on lightning counts from space and in situ measurements of NO in individual thunderstorms
lightning NOx in models often parameterised by cloud height or convective precipitation
the relevance of lightning NOx is that it is injected in the upper troposphere, where ozone formation is very efficient
http://thunder.nsstc.nasa.gov/data/OTDsummaries/

## Slide 18: NOx from Lightning: Example
NO2 columns retrieved from GOME satellite data
coincident measurements of clouds, lightning and NO2 in space and time
no indication for pollution impact
direct evidence without a priori assumptions
GOME trop. NO2SCD (1015 molec/cm2)
Cloud fraction
NLDN flashes (time of last lightning event)
Beirle et al., Estimating the NOx produced by lightning from GOME and NLDN data: a case study in the Gulf of Mexico Atmos. Chem. Phys., 6, 1075-1089, 2006

## Slide 19: Measurements of NOx
Challenges
high spatial and temporal variability
what is a representative measurement location?
vertical distribution
Techniques
in-situ using chemiluminescence
locally using absorption spectroscopy
globally using remote sensing in the visible spectral range

## Slide 20: in-situ NOx Measurements
Idea:
In some exothermic reactions, part of the energy is released as photons that can be measured by a photomultiplier.
O3 + NO -> NO2* + O2
NO2* -> NO2 + h
NO2* + M -> NO2 + M
The emitted intensity depends on the effectiveness of quenching which is proportional to the pressure and the concentrations of [O3] and [NO].
If pressure and [O3] concentration are kept constant, the intensity is proportional to the concentration of the NO.
O3
NO2

## Slide 21: Long Path DOAS measurements
open path through the atmosphere
lamp
telescope
retro reflectors
spectrometer
detector
quartz fibre
Instrument:
open path Differential Optical Absorption Spectroscopy (DOAS) system using a lamp as light source
retro reflectors for simplified set-up
white cells (multi reflection) for enhanced light path possible
advantages:
measurements at night
well defined light path
extension to UV (no ozone layer in between)
disadvantages:
relatively short light path
need for bright lamp (+ power)
usually not fully automated

## Slide 22: Satellite NO2 Measurements
DOAS analysis
Total Slant Column
Tropospheric Slant Column
Tropospheric Vertical Column
SCIATRAN RTM (airmass factor)

## Slide 23: Satellite NO2 Measurements: Example
anthropogenic pollution
biomass burning
ships
transport

## Slide 24: Satellite NO2 instruments
GOME-2 A and B
similar to GOME
launched 10.06 and 10.2012
80 x 40 km2 ground pixel
global coverage in 1.5 days
GOME
07.95 – 06.03 (full coverage)
4 channels 240 – 790 nm
0.2 – 04 nm FWHM
nadir viewing
320 x 40 km2 ground pixel
sun-synchronous orbit
global coverage in 3 days
SCIAMACHY
08.02 – 04.12
8 channels 240 – 1700 nm and 2 – 2.4 μm
0.2 – 04 nm (1.5 nm) FWHM
nadir viewing + limb + solar / lunar occultation
60 x 30 km2 typical ground pixel
sun-synchronous orbit
global coverage in 6 days
OMI
imaging spectrometer
launched 07.04
13 x 24 -120 x 24 km2 ground pixel
global coverage in 1 day
TROPOMI on Sentinel 5 Precursor
imaging spectrometer
launched 10.2017
Up to 3.5 x 7 km2 ground pixel
global coverage in 1 day

## Slide 25: NOx Emission Estimates
“bottom up”
using statistical data on activities (e.g. number and type of cars, average mileage, average fuel consumption)
and data on emission factors (x g NO emitted per l fuel)
“top down”
using measurements of e.g. NO2 or other species influenced by NOx
applying a model to establish the connection between emissions and atmospheric concentrations (or columns)
iterating emissions in the model to improve agreement between model prediction and measurements
the more measurements, the better => satellite data should be optimal, but accuracy and lack of vertical resolution is a problem

## Slide 26: Example: Bottom up Emission Estimates for China
Problem:
depending on the data source and approach used, emission inventories differ significantly
political considerations can interfere (in both directions)
→ comparison with independent data e.g. from satellites can help
Ma, J. et al., Comparison of model-simulated tropospheric NO2 over China with GOME-satellite data, Atmospheric Environment, 40, 593–604, 2006

## Slide 27: Example: Top Down Emission Estimates
Approach:
GEOS-CHEM model
GOME NO2 columns
linearized relation between NOx emission and NO2 column determined for each grid cell from model
error weighted combination of a priori (GEIA) and a posteriori emissions
improved emission inventory with reduced uncertainties
Martin, R. et al.,, Global inventory of nitrogen oxide emissions constrained by space-based observations of NO2 columns, J. Geophys. Res., 108(D17), 4537, doi:10.1029/2003JD003453, 2003.

## Slide 28: NOx Emission Trends
NOx emissions in
Europe, the US and
Japan are decreasing:
switch from coal and oil to natural gas
use of catalytic converters
“export” of heavy industry
As a result, NO2 levels
have fallen as expected,
but not the ozone levels.
http://www.environment-agency.gov.uk/commondata/103196/1162888?referrer=/yourenv/eff/1190084/air/1158715/1162725/
UK
1996
2002

## Slide 29: NOx reductions: Catalytic Converter
oxidation of hydrocarbons and CO on platinum 2CO + O2  2 CO2
In principle, if fuel would be fully oxidized, cars should only emit H2O and CO2. However, in practice not all hydrocarbons are oxidized and NO is formed from N2 and O2.
conversion of NO to N2 and O2 using H2 and CO from the exhausts on rhodium: 2NO N2 + O2

## Slide 30: Satellite NO2 Trends: The Global Picture
NO2 reductions in Europe and parts of the US
strong increase over China
consistent with significant NOx emission changes
7 years of GOME satellite data
DOAS retrieval + CTM-stratospheric correction
seasonal and local AMF based on 1997 MOART-2 run
cloud screening
1996 - 2002
GOME annual changes in tropospheric NO2
A. Richter et al., Increase in tropospheric nitrogen dioxide over China observed from space, Nature, 437 2005

## Slide 31: Satellite NO2 Trends: The Global Picture
A. Richter et al., Increase in tropospheric nitrogen dioxide over China observed from space, Nature, 437 2005
NO2 reductions in Europe and parts of the US
strong increase over China
consistent with significant NOx emission changes
7 years of GOME satellite data
DOAS retrieval + CTM-stratospheric correction
seasonal and local AMF based on 1997 MOART-2 run
cloud screening
1996 - 2002
GOME annual changes in tropospheric NO2

## Slide 32: Satellite NO2 Trends: The Global Picture
Hilboll, A., Richter, A., and Burrows, J. P.: Long-term changes of tropospheric NO2 over megacities derived from multiple satellite instruments, Atmos. Chem. Phys. 13, 4145-4169, doi:10.5194/acp-13-4145-2013, 2013

## Slide 33: Satellite NO2 Trends: Caveats
What can explain the observed increase in NO2 over China?
A GOME instrument drift
  => this should affect Japan as well but not SCIAMACHY
A change in viewing conditions as a result of changes in cloud cover, aerosol loading or vertical transport
  => there is no indication for this from the GOME data themselves
A change in NO to NO2 partitioning at constant NOx levels, for example as a result of a change in O3
A change in NO2 losses, for example as a result of decreased OH concentrations
An increase in NO2 concentrations as a result of increased NOx emissions

## Slide 34: Satellite NO2 trends: The last years
xx
2011 – 2016:
NO2 reduction nearly everywhere in China
Increase in NO2 in Taiwan, Russia, India
2011 - 2016
Longterm evolution:
NO2 maximum in 2011 – 2013
Then: rapid decrease
stabilisation in 2016
Data from all satellite instruments consistent

## Slide 35
van der A, R. J.et al. (2008), Trends, seasonal variability and dominant NOx source derived from a ten year record of NO2 measured from space, J. Geophys. Res., 113, D04302, doi:10.1029/2007JD009021.
Satellite NO2 Trends over large cities

## Slide 36
Satellite NO2 Trends over large cities
NO2 levels are changing in cities throughout the world. Contributing factors are
Urbanisation
Population growth
Increase in standard of living
changes in fuels used
Improvements in emission controls

## Slide 37
Satellite NO2 Trends over large cities
Vrekoussis, Met al., Economic crisis detected from space: Air quality observations over Athens/Greece, Geophys. Res. L ett., 40, doi:10.1002/grl.50118., 2013
Decreasing NO2 trend over Greek cities from 2007 – 2011
Both in satellite and surface data
Link to oil consumption
Effect of economic crisis

## Slide 38: NO2 Trends above Middle East
Do conflicts have an impact on NO2 pollution?
OMI data show consistent increase in NO2 levels throughout the Middle East from 2005 – 2010
Israel shows no increase (pollution reduction)
After 2010, large reductions are seen in many countries, in particular in Syria and Iran
Saudi-Arabia and Kuwait implemented air pollution control measures
Lelieveld, J., et al.: Abrupt recent trend changes in atmospheric nitrogen dioxide over the Middle East, Sci. Adv., 1(7), doi:10.1126/sciadv.1500498, 2015.
1015 molec cm2
2005 - 2010
2010 - 2014
1015 molec cm2

## Slide 39: NO2 Trends: Comparison with bottom up estimates
Q. Zhang et al., NOx emission trends for China, 1995–2004: The view from the ground and the view from space, J. Geophys. Res., 112, D22306, doi:10.1029/2007JD008684., 2007
the latest bottom-up inventories agree qualitatively with satellite data
summer values agree even quantitatively
satellite problems in winter?
strong seasonality in emissions?
How do the satellite derived trends compare to bottom up estimates?

## Slide 40: NO2 Trends: Comparison with bottom up estimates
Overall pattern in emission data base is correct
Increase in China is underestimated
Increase in India and Middle East is overestimated
Decrease in Europe / US is underestimated
GOME and SCIAMACHY
EDGAR v4.2
Hilboll, A., Richter, A., and Burrows, J. P.: Long-term changes of tropospheric NO2 over megacities derived from multiple satellite instruments, Atmos. Chem. Phys. 13, 4145-4169, doi:10.5194/acp-13-4145-2013, 2013

## Slide 41: NO2 Trends above Europe
How do the satellite derived trends compare to bottom up estimates?
GOME and SCIAMACHY data over Europe + CHIMERE
Comparison to two versions of EMEP emissions
Excellent agreement in some regions, disagreement in others
Konovalov, I.et al., Satellite measurement based estimates of decadal changes in European nitrogen oxides emissions, Atmos. Chem. Phys., 8, 2623-2641, 2008

## Slide 42: NOx Emissions from Shipping
Ship emissions:
large source of NOx, SOx and aerosols
relevant input into marine boundary layer
well defined NO2 patterns in Red Sea and Indian Ocean in GOME-2 data
consistent with pattern of shipping
With estimate of NO2 lifetime, NOx emissions can be estimated => agreement within error bars.
But: error bars still large (mainly from lifetime)
A. Richter et al., Satellite Measurements of NO2 from International Shipping Emissions, Geophys. Res. Lett., 31, L23110, doi:10.1029/2004GL020822, 2004
A. Richter et al..: An improved NO2 retrieval for the GOME-2 satellite instrument, Atmos. Meas. Tech., 4, 1147-1159, doi:10.5194/amt-4-1147-2011, 2011
Franke et al., Atmos. Chem. Phys., 9, 7289-7301, 2009

## Slide 43: Changes in NOx Emissions from Shipping
Trade and cargo volume is increasing
NO2 over shipping regions shows similar trend
Economic crisis in 2008 created clear signature in both, trade volume and shipping NOx
de Ruyter de Wildt, M., H. Eskes, and K. F. Boersma (2012), The global economic cycle and satellite-derived NO2 trends over shipping lanes, Geophys. Res.Lett., 39, L01802, doi:10.1029/2011GL049541.

## Slide 44: NOx Emission Trends: predictions
more or less constant in industrialised areas
increases in developing countries
large increases in Asia
large increases from shipping
Eyring et al., Atmos. Chem. Phys. Discuss., 6, 8553–8604, 2006

## Slide 45: Diurnal variation of NOx emissions
=> SCIAMACHY 10-40% higher than OMI for most anthropogenic source regions
=> SCIAMACHY lower than OMI for biomass burning regions
F. Boersma et al., Intercomparison of SCIAMACHY and OMI tropospheric columns:
observing the diurnal evolution of chemistry and emissions from space J. Geophys. Res., 113, D16S26, doi:10.1029/2007JD008816
SCIAMACHY: morning orbit (10:00 LT)
OMI: noon orbit (13:30 LT)
expected changes in
photochemistry => less NO2 around noon
emissions => depends on sources
SCIA – OMI tropospheric NO2 August 2006

## Slide 46: Diurnal variation of NOx emissions
Comparison with GEOS-Chem:
diurnal variation over biomass burning not correct
diurnal emission profile needs to be taken into account
better agreement is achieved
but: it’s only two points...
=> Geostationary needed
F. Boersma et al., Intercomparison of SCIAMACHY and OMI tropospheric columns: observing the diurnal evolution of chemistry and emissions from space J. Geophys. Res., 113, D16S26, doi:10.1029/2007JD008816

## Slide 47: Are Emissions changing from NO to NO2?
Conventional Wisdom:
all NOx is emitted as NO
rapid conversion to NO2 via reaction with O3
Recent Developments:
measurements hint at up to 20% of NO2 emissions
oxidizing particulate traps in diesel engines oxidize NO
this is going to increase!
Effects:
change in NO2 concentrations in rural areas
effect on top-down emission estimates
shift in NOx / NOy chemistry
David Carslaw. www.iaqm.co.uk/text/resources/no2_carslaw.pdf
Primary NO2 in London

## Slide 48: Summary
NOx (NO + NO2) in the troposphere is relevant for ozone chemistry, acid deposition
NOx emissions are both natural (soils, lightning, fires) and anthropogenic (fossil fuels, fires), the latter dominating
NOx can be measured in-situ, NO2 also by spectroscopic methods both locally and from satellite
satellite measurements provide interesting insights in many aspects of NOx emissions and chemistry
NOx emissions are changing with decreasing values in the already industrialised countries (improved technology, fuel changes) and increasing values in the industrialising countries (intensified used of fossil fuels) with some short term effects of economic crisis
technological changes can have unexpected results on NOx emissions (e.g. diesel engines, soot filters)
=> we are not going to run out of interesting NOx topics anytime soon!

## Slide 49
Thank you for your attention
and
questions please!
http://www.animationlibrary.com/animation/25494/Alarm_jumps/